## Slide 1
CSE 140L
Combinational circuits
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
Visiting Scholar UCSD
January 9, 2017

## Slide 2: Combinational circuit
A combinational circuit is a pure function, e.g., +, min, max,
It has no memory or state, i.e., given the same input it produces the same output
  Thus, a counter is not a combinational circuit
Inputs and outputs are binary – either 0 or 1
f

## Slide 3: Truth Table
The functionality of a combinational circuit can be defined using a Truth Table
It lists all possible combinations of values for inputs and specifies the output for each input
For every Truth Table there is a corresponding combinational circuit
a | b | c | s1 | s2
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0
f
a
b
c
s2
s1
What is the size of a truth table?

## Slide 4: Three simple combinational circuits
NOT
AND
OR
a | b | s
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a | b | s
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
a | s
0 | 1
1 | 0
Any combinational ckt can be built using these three gates
s = a∙b
s
a
s
a
b
s
a
b
s = ~a
s = a+b

## Slide 5: Some other famous gates
NAND
NOR
a | b | s
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a | b | s
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
s = ~(a∙b)
s = ~(a+b)
s
a
b
s
a
b
Can you express these gates using NOT, AND, and OR gates?
s
a
b
s
a
b

## Slide 6: Exclusive OR (XOR): another famous gate
XOR
From the Truth Table XOR produces a 1 when either (a=0) AND (b=1) or (a=1) AND (b=0). Hence, a  b = ~a.b + a.~b
a | b | s
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
s = a  b
s
a
b
Can you express XOR using NOT, AND, and OR gates?
s
a
b

## Slide 7: Nomenclature
We use the words in each of the following categories interchangeably
  combinational circuits, Boolean expressions, Boolean circuits
  gate, Boolean operator
We use variables to name wires in a combinational circuit

## Slide 8: Describing Complex Combinational ckts
A combinational ckt with n input variables and m outputs has 2n rows and m columns in its Truth Table representation
  Truth Tables are not a practical representation for circuits with large number of inputs
  Circuit diagrams are even more tedious and impractical
  Both representations are useless when we want computers to simulate the behavior of a circuit, i.e., determine the output given an input
We will use a programming language called Bluespec System Verilog (BSV) to express all ckts

## Slide 9: Half Adder
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Boolean equations
s = (~a∙b) + (a∙~b)
c = a∙b
“Optimized”
s = a  b

## Slide 10: Half Adder
function ha(a, b);
s = (!a & b) | (a & !b);
c = a & b;
return {c,s};
endfunction
“Structural” code – only specifies interconnection between boxes
-- order of statements does not matter.
Not quite correct –needs type annotations
Boolean equations
s = (~a∙b) + (a∙~b)
c = a∙b
OR
AND
NOT

## Slide 11: Half Adder corrected
function Bit#(2) ha(Bit#(1) a, Bit#(1) b);
Bit#(1) s = (!a & b) | (a & !b);
Bit#(1) c = (a & b);
return {c,s};
endfunction
“Bit#(1) a” type declaration says that a is one bit wide
{c,s} represents bit concatenation
How big is {c,s}?
2 bits

## Slide 12: “Optimized” Half Adder
function Bit#(2) ha(Bit#(1) a, Bit#(1) b);
Bit#(1) s = a ^ b;
Bit#(1) c = a & b;
return {c,s};
endfunction
XOR
“Optimized” (~a∙b) + (a∙~b) = a  b

## Slide 13: BSV notes
Suppose we write t = ha(a,b) then t is a two-bit quantity representing c and s values
We can recover c and s values from t by writing t[0] and t[1], respectively.
function Bit#(2) ha(Bit#(1) a, Bit#(1) b);
Bit#(1) s = a ^ b;
Bit#(1) c = a & b;
return {c,s};
endfunction

## Slide 14: Types
A type is a grouping of values:
  Integer: 1, 2, 3, …
  Bool: True, False
  Bit: 0,1
  A pair of Integers: Tuple2#(Integer, Integer)
  A function fname from Integers to Integers:
  function Integer fname (Integer arg)
Every expression in a BSV program has a type; sometimes it is specified explicitly and sometimes it is deduced by the compiler
Thus we say an expression has a type or belongs to a type
The type of each expression is unique

## Slide 15: Parameterized types: #
A type declaration itself can be parameterized by other types
Parameters are indicated by using the syntax ‘#’
  For example Bit#(n) represents n bits and can be instantiated by specifying a value of n
  Bit#(1), Bit#(32), Bit#(8), …

## Slide 16: Type synonyms
typedef bit [7:0] Byte;
typedef Bit#(8) Byte;
typedef Bit#(32) Word;
typedef Tuple2#(a,a) Pair#(type a);
typedef Int#(n) MyInt#(type n);
typedef Int#(n) MyInt#(numeric type n);
The same
The same

## Slide 17: Selecting a wire: x[i]
Constant Selector: e.g., x[2]
Dynamic selector: x[i]
[2]
x0
x1
x2
x3
no hardware; x[2] is just the name of a wire
4-way mux
assume x is 4 bits wide
x0
x1
x2
x3
i
[i]
x0
x1
x2
x3
x0
x1
x2
x3
i

## Slide 18: A 2-way multiplexer
(s==0)? A : B
A
B
S
Gate-level implementation
A mux is simple conditional expression
S
A
B

## Slide 19: A 4-way multiplexer
case {s1,s0} matches
0: A;
1: B;
2: C;
3: D;
endcase
s0
s0
s1
A
B
C
D

## Slide 20: Today’s Takeaways
“Combinational Circuits” are a form of “Digital Hardware”
  These circuits have no state, and thus, are pure functions
Common way to describe them is by Truth Tables or Circuit Diagrams but both have limitations (Why?)
Modern programming languages can make it easy to describe (complex) combinational circuits as an acyclic graph of gates, and allow us to simulate their behavior
We will use Bluespec System Verilog (BSV) in this class
  BSV is a high-level typed language where types can be parameterized, including for the number of inputs and outputs
  Every expression has a (unique) type in BSV.
  Type checking helps in avoiding many silly mistakes